## Slide 1
Report
Parking Guidance System Solution

## Slide 2
Project Information
Project name: Parking Guidance System Solution
Project Code: PGSS
Product Type: Internet of Things Application
Start Date: 3-Jan-2017
End Date:

## Slide 3
Our proposed solution is to build a parking guidance system with RF modules. The RF modules provide wireless communication directly between Central Control Unit and Detectors, Indicator LED, Information LED Displays so there is no need for the Zone Control Units.
A wireless Parking Guidance System utilize RF.
A server to keep track of data and information
A mobile app provides a simple and intuitive geolocation for drivers
Proposed Solution

## Slide 4
Feature Functions
Detector using Triple Axis Digital Compass Sensor
Information LED Displays for Main entrance and internal junction
A Mobile Application
Reservation Barrier
Indicator LED with RGB

## Slide 5
Block Diagram

## Slide 6
Use Case

## Slide 7
    System Overview Use Case

## Slide 8
    Manager Use Case

## Slide 9
    Administrator Use Case

## Slide 10
    End User Use Case

## Slide 12
Start
Setup nRF24L01+, read data from HMC5883L multiple times to get stabilized data, setup RGB led
Reserved?
Read data from nRF24L01+
Read data from HMC5883L
Car in range? 1st time
Change RGB LED to green
Change RGB LED to red
No
No
Yes

## Slide 13
Receive package?
Validated package?
Send ACK
Switch command
No
No
Yes
Yes

## Slide 14
Case RESERVE
Case LOT_Status
Case UNRESERVE
Send lot status package and wait for ACK
Received ACK?
Raise servo, update status to reserved, change RGB LED to red
Lower servo, update status to not reserved, change RGB LED to red
Yes
Yes
Yes
Resend 15 times?
No
No
Yes
Yes
No
Yes

## Slide 16
Start
Setup nRF24L01
Start polling all parking lot
Received ACK?
Start polling at information display
Send check status package, wait for ACK
Exists parking lot need to poll status
Not timeout?
Yes
Yes
Yes
No

## Slide 17
Received package?
Read data from nRF24L01+
Validated package?
Yes
Update lot status and area available lot
Send pubnub message and update server
Yes
No
No

## Slide 18
Exists one need to be updated
Send update information package, wait for ACK
Receive ACK?
Resend 15 times
No
No
Yes
Yes
Yes